## Slide 1: IT WORKSHOP
TASK-1
Identification of peripherals of a computer , components in a CPU and its functions. Draw the block diagram of the CPU along with the configuration of each peripheral.

## Slide 2: RAM( Random Access Memory)
RAM (Random Access Memory) is a type of computer memory that is used to temporarily store data and instructions that a computer's CPU (Central Processing Unit) needs to access quickly during program execution. RAM is a key component of a computer's memory hierarchy and plays a crucial role in determining system performance. Here's an overview of RAM and its types:
Purpose of RAM:
  RAM serves as a high-speed temporary storage medium that allows the CPU to quickly access data and instructions that are actively being used by running programs.
  Unlike storage devices such as hard disk drives (HDDs) or solid-state drives (SSDs), which provide long-term storage for data, RAM is volatile memory, meaning that its contents are lost when power is turned off.

## Slide 3: RAM
Functionality:
  RAM stores data in memory cells, which are organized into rows and columns.
  Each memory cell holds a binary digit (bit) of data, and multiple cells are grouped together to form bytes, which are the basic units of data storage.
  The CPU reads and writes data to RAM using memory addresses, which specify the location of data within the memory.
Types of RAM
DRAM (Dynamic RAM)
SRAM( Static RAM)

## Slide 4: ROM ( read only memory)
ROM, or Read-Only Memory, is a type of non-volatile memory used in computers and electronic devices to store data or instructions that are permanently written during manufacturing and cannot be easily modified or erased by the user.
ROM is primarily used to store firmware, BIOS (Basic Input/Output System), boot loaders, and other essential system software that is required for the operation of a computer or electronic device.
Unlike Random Access Memory (RAM), which loses its data when power is turned off, ROM retains its contents even when power is removed.

## Slide 5: Types of ROM
Mask ROM (MROM): The data in mask ROM is programmed during the manufacturing process using a mask that permanently defines the data pattern. Once programmed, the data cannot be changed or erased.
Programmable ROM (PROM): PROM allows users to program data into the memory after manufacturing using special programming devices called PROM programmers. Once programmed, the data becomes permanent and cannot be changed.
Erasable Programmable ROM (EPROM): EPROM can be programmed and erased multiple times using ultraviolet (UV) light. EPROM chips have a transparent quartz window on top that allows UV light to erase the data, making them reusable.
Electrically Erasable Programmable ROM (EEPROM): EEPROM allows data to be programmed and erased electrically using specialized programming signals. EEPROM can be reprogrammed in-circuit, making it suitable for applications where frequent updates are required.

## Slide 6: ROM
ROM is used in a variety of electronic devices, including computers, embedded systems, consumer electronics, and automotive systems.
In computers, ROM holds firmware and BIOS code that initializes the hardware and performs system-level tasks during the boot process.
In embedded systems, ROM stores essential software or configuration data needed for device operation, such as control programs for microcontrollers or settings for industrial machinery.
In consumer electronics, ROM may store firmware for devices such as digital cameras, printers, and smart appliances.

## Slide 7: HDD ( Hard disk drive)
A Hard Disk Drive (HDD) is a type of non-volatile storage device used to permanently store and retrieve digital data. HDDs have been a fundamental component of computer systems for several decades and are widely used in desktop computers, laptops, servers, and other electronic devices.
HDDs are used for various applications, including storing operating systems, software applications, documents, multimedia files, databases, and more.
They are commonly used in desktop computers, laptops, external storage devices, servers, network-attached storage (NAS) devices, and other electronic devices.

## Slide 8: SDD ( solid state drive)
An SSD, or Solid State Drive, is a type of storage device that uses flash memory to store data persistently. Unlike traditional Hard Disk Drives (HDDs), which use spinning magnetic disks to store data, SSDs have no moving parts and store data electronically.
SSDs are used in a wide range of applications, including desktop and laptop computers, gaming consoles, servers, workstations, and embedded systems.
They are particularly well-suited for tasks that require fast data access and high-performance storage, such as gaming, multimedia editing, virtualization, and data center applications.

## Slide 9: AGP slots
The AGP (Accelerated Graphics Port) slot was a specialized expansion slot found on older motherboards that was specifically designed for connecting graphics cards to a computer system.
Purpose:
  The AGP slot was introduced in the late 1990s as a dedicated interface for connecting graphics cards to the motherboard.
  It was designed to provide a high-speed, direct connection between the graphics card and the CPU/memory subsystem, allowing for improved graphics performance and efficiency.

## Slide 10: PCI slots
PCI (Peripheral Component Interconnect) slots are a type of expansion slot commonly found on motherboards, allowing users to connect various expansion cards to their computer systems.
Purpose:
PCI slots are designed to accommodate expansion cards that enhance the functionality of a computer system by adding features such as additional ports, connectivity options, or specialized processing capabilities.
Common types of expansion cards that can be installed in PCI slots include sound cards, network cards, USB expansion cards, SCSI controllers, and more.

## Slide 11: Processor
A processor, also known as a central processing unit (CPU), is the primary component of a computer responsible for executing instructions and performing calculations. It is often referred to as the "brain" of the computer because it interprets and executes instructions from software programs, operating systems, and user input.

## Slide 12: Components of Processor
A processor typically consists of several key components, including:Arithmetic Logic Unit (ALU): Performs arithmetic and logic operations, such as addition, subtraction, multiplication, division, and comparisons.
Control Unit: Coordinates the operation of the processor, fetching instructions from memory, decoding them, and controlling the execution of instructions.
Registers: Small, high-speed storage locations within the CPU used to store data temporarily during instruction execution.
Cache Memory: Fast, on-chip memory used to store frequently accessed data and instructions, reducing memory access times and improving performance.
Clock: Generates clock signals that synchronize the operation of various components within the CPU.

## Slide 13: North Bridge:
The North Bridge is responsible for handling communication between the CPU (Central Processing Unit) and high-speed components such as RAM (Random Access Memory) and the graphics card (if not integrated into the CPU).
It's like a traffic controller for data moving between the CPU and these high-speed devices.
The North Bridge also determines the type and speed of RAM that can be used with the motherboard.
It's called the "North" Bridge because it's usually located at the top of the motherboard, closer to the CPU.

## Slide 14: South Bridge:
The South Bridge is responsible for handling communication between the CPU and slower, peripheral devices such as hard drives, USB ports, audio devices, and network interfaces.
It's like a traffic controller for data moving between the CPU and these slower devices.
The South Bridge also manages input/output operations and provides support for legacy devices and interfaces.
It's called the "South" Bridge because it's usually located at the bottom of the motherboard, farther away from the CPU.

## Slide 15: Acronyms and their full forms
CPU - Central Processing Unit
GPU - Graphics Processing Unit
RAM - Random Access Memory
ROM - Read-Only Memory
CMOS - Complementary Metal-Oxide Semiconductor
BIOS - Basic Input/Output System
SATA - Serial Advanced Technology Attachment
PATA - Parallel Advanced Technology Attachment
USB - Universal Serial Bus
DDR - Double Data Rate

## Slide 16
AGP - Accelerated Graphics Port
PCI - Peripheral Component Interconnect
ATX - Advanced Technology eXtended
ITX - Information Technology eXtended
VRM - Voltage Regulator Module
LAN - Local Area Network
WLAN - Wireless Local Area Network
VGA - Video Graphics Array
HDMI - High Definition Multimedia Interface

## Slide 17
What is the purpose of the BIOS on a motherboard?
  BIOS initializes hardware components during startup and provides basic system configuration and control.
How does the chipset contribute to the functionality of a motherboard?
  The chipset manages communication between the CPU, memory, peripherals, and other components on the motherboard.
Explain the significance of expansion slots on a motherboard.
  Expansion slots allow users to add additional functionality to their system by installing expansion cards like graphics cards, sound cards, and network adapters.

## Slide 18
What is the role of RAM slots on a motherboard?
  RAM slots allow for the installation of RAM modules, providing temporary storage for data and instructions used by the CPU.
Describe the function of the CPU socket on a motherboard.
  The CPU socket is where the processor (CPU) is installed, allowing it to communicate with other components on the motherboard.
Why are power connectors essential components of a motherboard?
  Power connectors deliver electrical power from the power supply unit (PSU) to the motherboard and its components, ensuring proper operation.

## Slide 19
What factors should be considered when selecting a motherboard for a computer build?
  Compatibility with CPU and other components, expansion options, form factor, available features, and budget are important considerations.
Discuss the role of connectors such as SATA, USB, and audio jacks on a motherboard.
  These connectors allow for the connection of storage devices, peripherals, and audio equipment, expanding the functionality of the system.
What is the purpose of the CMOS battery on a motherboard?
  The CMOS battery provides power to the CMOS memory, which stores BIOS settings and system configuration data.

## Slide 20
How does a motherboard facilitate communication between hardware components?
Motherboards use buses and interfaces to facilitate communication between the CPU, memory, expansion cards, storage devices, and other peripherals connected to the system.
What is the function of the Northbridge and Southbridge chips on a motherboard?
The Northbridge traditionally managed high-speed communication between the CPU, RAM, and graphics card, while the Southbridge handled communication with slower peripheral devices.

## Slide 21
Discuss the significance of the PCIe slots on a motherboard.
PCIe slots allow for the installation of expansion cards such as graphics cards, network adapters, and storage controllers, providing high-speed data transfer between these devices and the CPU.